## Slide 1: WiFiMon: Experiences from Users
UbuntuNet Connect 2024, Dar es Salaam, Tanzania
October 31th, 2024
Elisantila Gaci, RASH, WiFiMon Service Manager

## Slide 3: Introduction
Monitoring Wi-Fi performance as experienced by end users
Combination of crowdsourced & hardware probe measurements
Contribution:
Detection of Wi-Fi throughput degradation
Determination of underperforming areas within a Wi-Fi network
 Admins may enhance performance, e.g. by installing more APs

## Slide 4: WiFiMon vs Related Monitoring Tools
Monitoring from the end-user perspective (end-user experience)
No requirements for app installation or end-user intervention
Centralized view of Wi-Fi performance available to the administrator

## Slide 5
Example: WiFiMon vs Ookla Speedtest
WiFiMon | Ookla Speedtest
Automatically by visiting a site | By pressing “GO”
Wi-Fi administrator | End users
Measurements are triggered:
Results collected by:

## Slide 6
WiFiMon Operation
WiFiMon Components:
WiFiMon Software Probes (WSPs)
WiFiMon Hardware Probes (WHPs)
WiFiMon Analysis Server (WAS)
WiFiMon Test Server (WTS)

## Slide 7: WiFiMon Users

## Slide 8: Main WiFiMon Users
ASNET-AM, Armenia
CERN, Switzerland
RENU, Uganda
Currently being tested in Brazil

## Slide 9: ASNET-AM (Armenia) Experiences from a conference pilot

## Slide 10: ASNET-AM Pilot Details (1/2)
Monitoring eduroam at the Institute for Informatics and Automation Problems (IIAP) - National Academy of Sciences of Armenia
Monitoring between September 21st - October 3rd 2023
Monitoring about 50-100 people (researchers, professors, engineers, students)
Measurements from 1 WHP (Raspberry Pi 4 Model B) – placed on the floor
WAS/WTS installed in a single VM with 4 vCPU’s, 8 GB RAM (WiFiMon v. 2.1.0)
Pilot Goal:
Experiment with newly introduced WiFiMon features
Help ASNET-AM Wi-Fi administrators identify interesting points requiring further inspection

## Slide 11: ASNET-AM Pilot Details (2/2)
Monitored area blueprints: WHP is placed at the green bullet

## Slide 12: Overview of WiFiMon Measurements (1/8)
The Overview tab summarizes received measurements on a daily basis

## Slide 13: Overview of WiFiMon Measurements (2/8)
The Overview tab summarizes received measurements on a daily basis
Total number of received measurements (since midnight)

## Slide 14: Overview of WiFiMon Measurements (3/8)
The Overview tab summarizes received measurements on a daily basis
Average download throughput reported

## Slide 15: Overview of WiFiMon Measurements (4/8)
The Overview tab summarizes received measurements on a daily basis
Minimum download throughput reported

## Slide 16: Overview of WiFiMon Measurements (5/8)
The Overview tab summarizes received measurements on a daily basis
Maximum download throughput reported

## Slide 17: Overview of WiFiMon Measurements (6/8)
The Overview tab summarizes received measurements on a daily basis
Metrics for Upload Throughput

## Slide 18: Overview of WiFiMon Measurements (7/8)
The Overview tab summarizes received measurements on a daily basis
HTTP ping metrics

## Slide 19: Overview of WiFiMon Measurements (8/8)
The WiFiMon Analysis Server (WAS) received 4717 total measurements on 11 days and 429 measurements per day on average
Loss of measurements is evident in various days (e.g. maximum loss on Oct 3rd)
Total number of WiFiMon performance measurements received daily between Sep 23rd and Oct 3rd

## Slide 20: WiFiMon Performance Measurements
WiFiMon may report various types of performance measurements (against the WiFiMon Test Server – WTS)
The most important are:
Download Throughput
Upload Throughput
HTTP Ping Round-Trip Time (RTT)
Jitter

## Slide 21: Average Download Throughput – Per Test-Tool
Average download throughput during the last 10 days:
NetTest reports interesting performance drops
LibreSpeed Speedtest reports rather stable performance
Akamai Boomerang detects a very interesting performance drop during the 27th of September; performance suddenly drops and almost stabilizes on a lower value
3 different test-tools were used (NetTest, Akamai Boomerang & LibreSpeed Speedtest)

## Slide 22: Average Download Throughput – Aggregated
Average download throughput during the last 10 days:
Interesting points (blue circles) can be seen in the diagram
Wi-Fi administrators may further inspect what happened at these points
The results of all test-tools are aggregated

## Slide 23: Average Upload Throughput – Aggregated
Average upload throughput during the last 10 days:
Significant drops (blue circles) are also visible in the chart
The results of all test-tools are aggregated

## Slide 24: A Closer look on October 3rd Measurements
Download throughput presumably dropped because of data uploads
Average download throughput
Average upload throughput

## Slide 25: Average HTTP Ping RTT - Aggregated
Average HTTP Ping RTT during the last 10 days:
Higher RTT’s are visible (blue circles) in the chart
The results of all test-tools are aggregated

## Slide 26: Average Jitter
Average Jitter during the last 10 days:
A very high jitter measurement (blue circle) is visible on October 2nd

## Slide 27: Average Link Quality
Average link quality during the last 10 days reported from the WLAN NIC of the probe:
Link quality (WLAN NIC) does not capture the drops reported by WiFiMon
A major drop on October 2nd matches the jitter increase (previous slide)

## Slide 28: Average Number of Users
Average number of Wi-Fi users during the last 10 days (reported by arp-scan):
Almost no users during the weekend (blue rectangle)
Higher number of users during the conference days (green rectangle)

## Slide 29: WiFiMon Performance Measurements
Apart from average measurements, WiFiMon may also report:
Median values
Maximum values
Minimum values
95th percentile values

## Slide 30: Average vs Max HTTP Ping RTT
Comparison between the average and the maximum HTTP Ping RTT:
Maximum values of RTT are much higher than the reported average

## Slide 31: CERN (Switzerland) Experiences reported in a published article (article)

## Slide 32: CERN Setup Details
Thousands of users (researchers, visitors, students, etc.)
Roughly 5000 Access Points
Both WiFiMon Hardware Probes (WHP’s) and WiFiMon Software Probes (WSP’s) are used

## Slide 33: CERN Crowdsourced Measurements
WSP measurements collected from 4 clients within the CERN’s Wi-Fi network

## Slide 34: CERN Hardware Probe Measurements
WHP measurements collected from 4 locations within the CERN’s Wi-Fi network

## Slide 35: WiFiMon Helped CERN Resolve Wi-Fi Issues
The reported Round Trip Time (RTT) and packet loss helped CERN identify an issue in the Wi-Fi configuration

## Slide 36: RENU (Uganda) Experiences reported during an infoshare (article)

## Slide 37: RENU Setup Details
Thousands of users
Both WHP and WSP measurements are considered

## Slide 38: WiFiMon Helped RENU Resolve Wi-Fi Issues
Results reported by two WiFiMon Hardware Probes (WHP’s) using multiple WiFiMon test tools

## Slide 39: Thank You